## Slide 1: ErgoSystems presents . . .
A Practical Approach to Office and Home Office Ergonomics
Mark Anderson, PT, CPE
Physical Therapist and Ergonomist
ErgoSystems Consulting

## Slide 2: Instructor Background/Experience
Mark A. Anderson, MA, PT, CPE
  Founder of Minneapolis, Minnesota based ErgoSystems Consulting, LLC
  Industrial Rehabilitation clinical practice in mid 1980’s led to interest in ergonomics
  Since 1993 certified by Board of Certification in Professional Ergonomics as Certified Professional Ergonomist (www.bcpe.com)
  Consulted in ergonomics for over 30 years
  Education
    Bachelor of Science Degree from University of North Dakota Physical Therapy program
    Master of Arts Degree in Physical Therapy from the University of Iowa
Notes: Instructor Background and Experience
Mark A. Anderson, MA, PT, CPE is the founder of Minneapolis, Minnesota based ErgoSystems Consulting, LLC.
Work in an Industrial Rehabilitation clinical practice in mid 1980’s led to his interest in ergonomics.
Since 1993 Anderson has been certified by the Board of Certification in Professional Ergonomics as Certified Professional Ergonomist (www.bcpe.com).
He has consulted in ergonomics for over 30 years
His education includes a Bachelor of Science Degree from the University of North Dakota Physical Therapy program and a Master of Arts Degree in Physical Therapy from the University of Iowa.
Anderson worked with WorkWell developing the Office and Manufacturing Ergonomics courses and the ERGONOMICS ON-DEMAND series.

## Slide 3: What do you want to accomplish?
Describe successful office workspace . . .

## Slide 4: A careful examination
Look carefully at the words
Do you see any pattern or trend?
Is there a predominant theme?

## Slide 5: In other words . . .
Words like comfort or comfortable mixed in with:
  Productive
  Efficient
  Satisfying
  Effective
  Safe and so on
Comfort . . . direct positive relationship to other descriptors

## Slide 6: Maximize comfort?
The answer is NO!
Maximizing comfort can be very dangerous thing to do . . .
Optimize comfort in workplace!

## Slide 7: Office Ergonomics Workstation Evaluation Form

## Slide 8: Chair
Objectives of chair
  Support body and limbs to provide relief from weight bearing
  Provide stable base or platform for body and limbs
  Position user at correct height and reach relationship to worksurface and tasks at hand
  Allow for easy change in position/movement of user

## Slide 9: Adjustment anxiety
Chairs can be pretty expensive
  All kinds of bells and whistles
  Chair only as good as how it is adjusted
Some people have never adjusted their chair
  Just sit down and go to work!
Bottom line
  Need to initially be able to adjust chair to fit
  As well as throughout day

## Slide 10: Seatpan Height
Does the chair’s seatpan height adjust up and down?

## Slide 11: Seatpan Tilt
Does chair’s seatpan tilt up and down?

## Slide 12: Seatpan Tension
Can you adjust seatpan tension?

## Slide 13: Seatpan Depth
Does the chair’s seat move forward or backward?

## Slide 14: Seatpan Fit
Does chair’s seat fit body size?

## Slide 15: Back Support Height
Does chair’s back support move up and down?

## Slide 16: Back Support Angle
Does chair’s back rest angle forward or backward?

## Slide 17: Cushion
Suitable cushion
  Foam density
  Wearability
  Breathability
  Type of material (fabric or rubberized)

## Slide 18: Armrests Adjust
Do chair’s armrests adjust up and down and/or side-to-side?

## Slide 19: Maintenance
Is chair functioning properly?
No maintenance problems?

## Slide 20: Sitting styles
Sitting styles quite varied from person to person:
  Percher
  Slouch
  Sit crossed leg
  Sit on leg

## Slide 21: Functional seated positions
Provide for several different acceptable postures
Rotate throughout day on regular basis
  Upright “keyboard” position
  Semi-reclined/rocking “conversation” position
  Standing

## Slide 22: Chair

## Slide 23: Worksurface
Worksurface objectives
  Provide functional workspace (depth, width)
  Support and position equipment
  Provide access to work materials
  Achieve desired relationship match between user/work

## Slide 24: Wrong Desk height
If work height is adjustable, adjust it as needed
  Raise height of work surface by putting it up on blocks
  Make sure desk or work surface is solidly placed on blocks and won’t fall off!
Adjust chair height
  Make sure feet are supported either on floor or with footrest
Add height/angle adjustable keyboard tray
  Mounted underneath work surface

## Slide 25: Sit/Stand Workstations
Portable systems placed on desk
  Adjustable keyboard/mouse and monitors
  Use chair when seated

## Slide 26: Sit/Stand Workstations
Height adjustable, user controlled, powered sit/stand workstations

## Slide 27: Worksurface

## Slide 28: Foot Support
In ideal world best foot support when seated in a chair is floor . . .
However, if needed use proper sized footrest

## Slide 29: Knee/foot clearance
Move what is not needed to some other storage position or get rid of it
Survey work area and determine what is blocking access

## Slide 30: Foot Support/Clearance

## Slide 31: Computer Equipment

## Slide 32: Keyboards
Keyboard configurations
  Straight-line
  Curved
  Articulated
Keyboard surface finish
Keyboard size
Keyboard activation pressure
Layout
Wireless

## Slide 33: Keyboard Technique
Free float piano playing style
Use of worksurface for forearm support

## Slide 34: Keyboard Solutions
Based on technique obtain correct height, reach and angle of keyboard
Adjust keyboard height and position
  Adjust worksurface height
  Keyboard tray
If cannot adjust keyboard height, position chair height to place hands in neutral posture in relation to keyboard
  May require support for feet if no longer touch floor

## Slide 35: Take break
Add stretching to day
  A little post it note put on computer monitor
  Software that reminds you to stretch
  Old-fashioned as egg timer
  Team up with someone else in office
  Take advantage of natural breaks between activities
Remember to Stretch!

## Slide 36: Stretching – Guidelines
Absolutely have to follow doctor's orders for any restricted activities
Technically correct
Energy Input/Output
Neutral Position
Joint Noises
Don’t hold breath
Regular and Consistent
Intensity/Controlled Stretching
Back Bend
Elbow Pull
High Reach
Large Arm Circles

## Slide 37: Keyboard Trays
Keyboard tray configurations
Keyboard tray size
Height adjustment
Angle adjustment
Knee clearance

## Slide 38: Keyboard Tray

## Slide 39: Keyboard

## Slide 40: Pointing device
No not that kind of mouse!
Use mouse as little as possible
  Keyboard shortcuts

## Slide 41: Pointing Device Technique
Neutral positions
  Same plane as keyboard
Mousing style or technique
  Free float piano playing style
  Use of worksurface for forearm support

## Slide 42: Mouse

## Slide 43: Computer
Desktop or laptop
Where?
  Easy access

## Slide 44: Computer

## Slide 45: Monitor
Everything need access to may be viewed through monitor
Watch people looking at their monitors
  Almost like monitor is a vacuum cleaner
  They turn it on . . . and it sucks their head right in!

## Slide 46: Monitor Alignment
Directly face primary work task
  Primarily data creation or manipulation
  Monitor directly in front

## Slide 47: Monitor Height
Where do we naturally read?
We read looking out and down

## Slide 48: Monitor Height
Top of screen no higher than eye level
Look out and use downward eye movement to look at lower part of screen

## Slide 49: Monitor Distance
Eyes
  Accommodation and Convergence
  Demomstration
Guideline
  Get screen as far away from user as possible
    At least arm’s length
    Still be able to read it clearly with good posture

## Slide 50: Monitor Size
Ultra-wide monitors
  Position windows as screens
  Simulate dual monitors
    Primary/Primary
    Primary/Secondary

## Slide 51: Dual Monitors
Primary/Primary
Primary/Primary

## Slide 52: Dual Monitors
Primary/Secondary
Primary/Secondary

## Slide 53: Eye Examinations
Regular eye examinations
  Eyewear prescriptions changes
  Eye health in general
  Based on job task

## Slide 54: Monitor

## Slide 55: Document holder
Horizontal vs. inclined

## Slide 56: Document Holder

## Slide 57: Telephone
Headsets
  Wireless
  Bluetooth

## Slide 58: Webcam
Webcam
  Location with comfortable position for head/neck
  Laptop or separate camera
Notes: Webcams have become an important consideration in your office. Whether the webcam is part of your laptop or a separate camera, make sure you are following the ergonomics principles of neutral head and neck position when you setup and use the webcam.
Fill out the Worksheet for Telephone/Webcam Features, Issues and Recommendations.

## Slide 59: Telephone/Webcam

## Slide 60: Office equipment
Make use of principles to position office equipment
  Calculator
  Printer
  Fax
  Writing utensils
  Scissors
  Paper clips
  Stapler
  Other Stuff

## Slide 61: Storage/Reach zone
Primary
  Frequently accessed from seating system
  Within easy reach
Secondary
  Occasionally accessed
  Located in gray zone
  Danger Zone!
Tertiary
  Very occasionally accessed
  Have to get up and move to access

## Slide 62: Storage

## Slide 63: Lighting – General and Task

## Slide 64: Illumination

## Slide 65: Recommended Specifications

## Slide 66: Home Office Ergonomics
Working at home on your computer?
  You aren’t alone!
  Many people who normally work at desk at work now work at home!
Tips and Techniques

## Slide 67: Setup of Your Home Office
Setup considerations:
  Location of office
  Sharing – partner/kids
  Computer equipment
    Laptop or desktop
  Desk/table
    Adjustable or fixed height
  Chair
    Adjustable or fixed position
  Physical comfort - promote
  Visual comfort - promote

## Slide 68: Step-by-Step Approach
Each setup will be somewhat unique!
Need to consider:
  “What is possible!”
  “Be creative!”

## Slide 69: Step-by-Step Approach - Location
What are your options?
  Dedicated space
    Yours only or shared space
      Partner/kids
    Desk/chair
    Privacy – visual and auditory
  Shared space
    Multi-purpose
    Kitchen/dining table and chair
    Setup and take down

## Slide 70: Step-by-Step Approach –Desk/Chair
Work through desk/chair options:
  Adjustable height table/desk and adjustable height chair
  Fixed height table/desk and adjustable height chair
  Fixed height table/desk and fixed height chair
  Couch
  Standing

## Slide 71: Step-by-Step Approach – Desk/Chair
Adjustable height table/desk and adjustable height chair
  First adjust chair height to place feet directly on floor
  Adjust table/desk height so wrists are straight when hands on keyboard
  Adjust monitor appropriately
  You are good to go!

## Slide 72: Step-by-Step Approach – Desk/Chair
Fixed height table/desk and adjustable height chair
  Place keyboard/mouse or laptop on fixed heightdesk/table
  Adjust chair height so wrists are straight with hands on keyboard
    If feet come off floor, find a box or stool so feet are not dangling
  Adjust monitor appropriately
  You are good to go!

## Slide 73: Step-by-Step Approach – Desk/Chair
Fixed height table/desk and fixed height chair
  Sit in chair and able to:
    Sit all way back in chair with lower back supported AND
    Feet on floor AND
    Wrists straight with keyboard use
  You are good to go!

## Slide 74: Step-by-Step Approach – Desk/Chair
Fixed height table/desk and fixed height chair
  Sit in chair, if wrists are not straight with keyboard use
    Need to adjust seated height
      Look for a different height chair
      Put a seat cushion in chair
    If this caused feet to come off floor
      Find box or stool so feet are not dangling
  If you are taller individual and table/desk too low
    May be able to put blocks under desk legs to raise it up
  Adjust monitor appropriately

## Slide 75: Step-by-Step Approach – Couch
Are we saying never sit on couch or easy chair and use laptop?
  The answer is no!
You can certainly some of the time use couch or recliner
  Use pillows under arms to provide support for arms and shoulders
  May place pillow under laptop to ensure straight wrists with keyboard
  Angle monitor so for viewing with least amount of head tip forward
  Sofa servers may work to position laptop
  Make sure feet and legs are well supported

## Slide 76: Step-by-Step Approach – Standing
As possible, mix in standing when using laptop or desktop
  Look for counter or place box on counter
  Stand comfortable tall with elbows about 90 degrees
  Wrists straight
  Angle laptop monitor
Good shoes are important for standing
  Good walking shoes will be good for standing
  Use footrest to alternate one foot up on rest

## Slide 77: Ergonomics – A Potent Tool!
Great number of factors in office ergonomics workplace!
Use ergonomics process to offer solutions that are practical and effective!
Be more comfortable!

## Slide 78: Thanks for your time and attention!

## Slide 79: ErgoSystems presents . . .
A Practical Approach to Office and Home Office Ergonomics
Mark Anderson, PT, CPE
Physical Therapist and Ergonomist
ErgoSystems Consulting