Equipment Checklist

"YES" response indicates potential problem areas that should receive further investigation.

| Foot/knee control pedals |
| --- |
| Does the operator have to operate foot/knee pedals while standing? | YES | NO | NA |
| To operate foot pedals or knee switches, must the worker assume an unnatural or uncomfortable posture? | YES | NO | NA |
| Are pedals too small to allow the operator to alter the position of the foot/knee? | YES | NO | NA |
| Are pedals triggered at a high repetition rate? | YES | NO | NA |
| Hand controls |
| Hand controls placed to not allow neutral hand/arm/body position? | YES | NO | NA |
| Hand controls difficult (require excessive force) to operate? | YES | NO | NA |
| Hand controls not properly designed to take into account amount and types of force required for operation? | YES | NO | NA |
| Do workers have to exert high levels of power grip force to operate equipment? | YES | NO | NA |
| Do workers have to exert high levels of pinch grip force to operate equipment? | YES | NO | NA |
| Position - Sustained/Awkward |
| To operate equipment, must worker maintain same body posture (either sitting or standing) all or most of the time? | YES | NO | NA |
| Is the pace of material handling determined by the equipment? (Feeding machines, conveyors, etc.) | YES | NO | NA |
| Does equipment operation require worker to repeat same movement pattern of arm/hand at a high rate of speed? | YES | NO | NA |
| Does equipment operation require continuous use (or nearly so) of both hands and both feet in order to operate controls or manipulate work object? | YES | NO | NA |
| Vibration - Whole body |
| Is the body as a whole subjected to vibration from exposure to or operation of the equipment? | YES | NO | NA |
| Equipment Preventive Maintenance |
| Is there not a regular maintenance schedule? | YES | NO | NA |
| Is the equipment designed or placed in such a way that cleaning and maintenance activities are not facilitated? | YES | NO | NA |

OVER TO ADD COMMENTS

COMMENTS